## Slide 1: Optimization of Traffic Signal Timing for Urban Intersections

## Slide 2: Introduction
Urban Traffic Challenges Urban intersections are critical points in road networks where traffic congestion often peaks, leading to increased travel time, fuel consumption, and air pollution. Inefficient signal timing is a major contributor to these challenges.
Need for Optimization With rapid urbanization and rising vehicle numbers, optimizing traffic signal timing is essential to ensure smoother traffic flow, minimize delays, and improve overall road safety and efficiency.
Objective of the Study This project focuses on developing data-driven and algorithmic approaches to optimize traffic signal timing at urban intersections. By leveraging intelligent traffic management systems and simulation tools, the goal is to enhance mobility and reduce congestion in city environments.

## Slide 3: Problem statement
Current Scenario Urban intersections often operate on fixed or outdated signal timings that do not adapt to real-time traffic conditions. This results in:
Increased traffic congestion
Long vehicle queues and delays
Higher fuel consumption and emissions
Reduced road safety and commuter satisfaction
Core Problem The lack of dynamic and data-driven traffic signal control leads to inefficient traffic management, especially during peak hours or unpredictable traffic surges.
Need for Solution There is a pressing need to optimize traffic signal timing using intelligent algorithms and real-time data to ensure smoother traffic flow and sustainable urban mobility.

## Slide 4: Objectives of the Research
The main objectives of this study are to:
Analyze current traffic signal timing strategies at urban intersections.
Identify key factors influencing traffic flow and delays during peak and off-peak hours.
Develop an optimization model using data-driven and intelligent algorithms (e.g., machine learning, metaheuristics).

## Slide 5: Research Questions
The optimization of traffic light timings at intersections within urban areas involves critical concerns regarding traffic efficiency, flexibility, and sustainability. Thus, to form the basis of such an investigation, the following sets of research questions:
RQ.1 How would be optimizing traffic signal timings affect the reduction of vehicle delays and urban intersection congestion vehicles?
RQ.2 What optimization techniques machine learning, play best with dynamic traffic signal control?

## Slide 6: Literature review
Ref | Focus Area | Methodology / Algorithm | Simulation Tool | Key Outcomes / Contributions
[1] | Multi-objective signal optimization | Genetic Algorithm, Pareto optimization | General, Cell Transmission Model | Highlights spillover prevention, scalability challenges
[2] | Real-time signal optimization | Swarm Intelligence Algorithm | MATLAB | Delay ↓10.25%, Stops ↓24.55%, Capacity ↑3.56%
[3] | Expressway off-ramp signal timing | Improved Genetic Algorithm | VISSIM, MATLAB | Stops ↓29.0%, Delay ↓27.8%, Queues ↓23.7%
[4] | Urban trunk line traffic | FASM-MDEA (fuzzy + MDEA) | Simulation-based | Reduced congestion, coordinated signal control
[5] | Mixed traffic (vehicles, pedestrians) | Improved PSO | Not specified | Delay and stops ↓, Capacity ↑
[6] | Large-scale network control | Multi-agent system, mathematical programming | MATLAB, VISSIM | Network oversaturation prevented, improved speed
[7] | Connected vehicles optimization | Enumeration & Pseudospectra methods | Simulation-based | Travel time ↓, Fuel economy ↑
[8] | Coordinated intersections | Real-time adaptive model | Case study (Bari, Italy) | Queues ↓, traffic flow ↑

## Slide 7
[9] | Oversaturated urban networks | Custom queue balancing algorithm | Not specified | Higher outflow, delay ↓, scalable approach
[10] | Isolated intersection optimization | GA + PSO hybrid | Traffic simulation tool | Traffic efficiency ↑, emissions ↓
[11] | CAV trajectory + signal optimization | Adaptive phasing & trajectory control | Closed track simulation | Speed ↑9%, Fuel ↓17-21%
[12] | Eco-efficient signal optimization | Simheuristic: SUMO + GA | SUMO | CO ↓4.97%, NOx ↓2.5%, PMx ↓3.83%
[13] | Fuel-optimal trajectories | Eco-driving model + SPaT data | INTEGRATION | Fuel ↓13.8%, scalable system
[14] | Signal cycle optimization | Multi-objective fixed-step search | Real-world data | Delay ↓, capacity ↑
[15] | Adaptive network-wide control | MIMO model + Adaptive LQR | 35-intersection simulation | Delay ↓, energy use ↓
[16] | Intersection efficiency with VANET | Ant Colony Optimization | Simulations (not named) | CO₂, noise, fuel ↓ in dense traffic
[17] | Fuzzy control for grouped signals | Distributed fuzzy + Simulated Annealing | Simulation | Better flow coordination, success index ↑
[18] | Multi-intersection congestion | Enhanced PSO + statistical model | Local data-based simulation | Queues ↓, better flow balancing
[19] | Multi-intersection optimization | Deep Reinforcement Learning (Graph Conv. Net) | SUMO | Delay ↓, model outperforms others
[20] | Urban congestion optimization | Simulated Annealing + PSO (SA-PSO) | 9-intersection network | Delay ↓41%, Stop rate ↓30.6%

## Slide 8: Methodology
1. Data Collection
Time step, Location, and traffic flow data collected from urban intersections
Use of sensors, cameras, or open-source datasets
2. Traffic Pattern Analysis
Identify peak/off-peak trends
Analyze queue lengths, delays, and saturation flow rates
3. Model Development
Formulation of optimization problem (e.g., minimize total delay or queue length)
Use of algorithms like Machine Learning algorithms and deep learning algorithms.
4. Evaluation
Compare performance metrics: average delay, travel time, fuel usage
Validate results against real or historical data

## Slide 9: Methodology Modelling
1. Data Preprocessing
Cleaning and normalization of traffic signal and vehicle flow data
Feature engineering: Time step, Location, and traffic flow data
2. Model Selection
Random Forest Regressor (RFR): Ensemble-based model for handling non-linear traffic patterns and predicting signal delay times
XGBoost Regressor (XGBR): Gradient boosting framework for accurate traffic flow prediction with feature importance analysis
Long Short-Term Memory (LSTM): A deep learning model designed to capture temporal dependencies and trends in sequential traffic data
Gated Recurrent Unit (GRU): Lightweight alternative to LSTM for forecasting traffic signal metrics with reduced computational complexity

## Slide 10: Model evaluation
Training and Validation
Split dataset into training and testing sets
Use cross-validation to evaluate model performance
Metrics: RMSE, R² Score

## Slide 11: Model Performance Overview
Model | R2 Score | RMSE | Remarks
Random Forest | 0.9137 | 0.0657 | Strong performance; good trade-off between accuracy and interpretability.
XGBoost | 0.9263 | 0.0607 | Best R² score; excellent accuracy; ideal for production deployment.
LSTM | 0.8902 | 0.0539 | Lowest RMSE; suitable for minimizing error; slightly lower R².
GRU | 0.8863 | 0.0546 | Close to LSTM; slightly lower performance in both metrics.
The models were evaluated based on the usual performance metrics, including R2 Score, RMSE. The following tabular format discusses the performance of each of the algorithms on the traffic dataset in predicting congestion levels.

## Slide 12: Conclusion
XGBoost achieved the best overall performance with the highest R² score (0.9263) and a low RMSE (0.0607), making it the most suitable model for traffic signal optimization.
Random Forest closely followed with an R² score of 0.9137 and RMSE of 0.0657, providing a reliable and interpretable alternative.
LSTM recorded the lowest RMSE (0.0539) but a slightly lower R² score (0.8902), indicating strong predictive accuracy with modest variance explanation.
GRU also performed well with RMSE of 0.0546 and R² score of 0.8863, making it a viable option for capturing sequential patterns in traffic data.
Conclusion:
XGBoost is the most balanced and accurate model, with Random Forest as a strong backup. LSTM and GRU remain useful for deep learning-based solutions depending on specific system requirements

## Slide 13: Future work
Incorporate additional features such as weather conditions, road incidents, and public events to enhance prediction accuracy.
Implement real-time data streaming and model retraining pipelines for live traffic signal adjustment.
Explore hybrid models that combine tree-based and deep learning approaches to leverage both interpretability and temporal pattern recognition.
Deploy models on edge devices or cloud-based infrastructure for scalable and responsive traffic management systems.
Evaluate model performance across multiple intersections and cities to ensure generalizability and robustness.
Integrate reinforcement learning for dynamic traffic signal control based on predicted congestion levels.

## Slide 14: References
Xu, Guilong, Zhen Yang, Shikun Xie, Shumin Bai, and Zishuo Liu. "Enhancing safety and efficiency of signal intersections: A part-time protected right-turn signal control for straight-right lane in connected environment." Physica A: Statistical Mechanics and its Applications (2025): 130378.
Fu X, Gao H, Cai H, Wang Z, Chen W. How to Improve Urban Intelligent Traffic? A Case Study Using Traffic Signal Timing Optimization Model Based on Swarm Intelligence Algorithm. Sensors. 2021; 21(8):2631. https://doi.org/10.3390/s21082631
Liu, S., Li, Y., Qiu, Y. et al. Signal Timing Optimization Algorithm for an Intersection Connected with an Urban Expressway. Arab J Sci Eng 45, 8667–8684 (2020). https://doi.org/10.1007/s13369-020-04835-6
H. Lin, Y. Han, W. Cai and B. Jin, "Traffic Signal Optimization Based on Fuzzy Control and Differential Evolution Algorithm," in IEEE Transactions on Intelligent Transportation Systems, vol. 24, no. 8, pp. 8555-8566, Aug. 2023, doi: 10.1109/TITS.2022.3195221.
Zhao, H., Han, G. & Niu, X. The Signal Control Optimization of Road Intersections with Slow Traffic Based on Improved PSO. Mobile Netw Appl 25, 623–631 (2020). https://doi.org/10.1007/s11036-019-01225-7
Pavan, D. S., Ronak R. Jain, Tirthankar Karmakar, and N. Chaitra. "Density-Based Traffic Signal Control System." In 2025 International Conference on Intelligent and Innovative Technologies in Computing, Electrical and Electronics (IITCEE), pp. 1-6. IEEE, 2025.
B. Xu et al., "Cooperative Method of Traffic Signal Optimization and Speed Control of Connected Vehicles at Isolated Intersections," in IEEE Transactions on Intelligent Transportation Systems, vol. 20, no. 4, pp. 1390-1403, April 2019, doi: 10.1109/TITS.2018.2849029.

## Slide 15
Faqir, Nada, Yassine Ennaji, Loqman Chakir, and Jaouad Boumhidi. "Hybrid CNN-LSTM and Proximal Policy Optimization Model for Traffic Light Control in a Multi-Agent Environment." IEEE Access (2025).
Tran, Q.H., Do, V.M. & Dinh, T.H. Traffic signal timing optimization for isolated urban intersections considering environmental problems and non-motorized vehicles by using constrained optimization solutions. Innov. Infrastruct. Solut. 7, 299 (2022). https://doi.org/10.1007/s41062-022-00895-9
H. Liu, C. E. Flores, J. Spring, S. E. Shladover and X. -Y. Lu, "Field Assessment of Intersection Performance Enhanced by Traffic Signal Optimization and Vehicle Trajectory Planning," in IEEE Transactions on Intelligent Transportation Systems, vol. 23, no. 8, pp. 11549-11561, Aug. 2022, doi: 10.1109/TITS.2021.3105329.
S. S. S. Mohiuddin Qadri, A. Almusawi, M. Albdairi and E. Esirgün, "Optimizing Traffic Signal Timing at Urban Intersections: A Simheuristic Approach Using GA and SUMO," 2024 Innovations in Intelligent Systems and Applications Conference (ASYU), Ankara, Turkiye, 2024, pp. 1-6, doi: 10.1109/ASYU62119.2024.10757086.
H. Yang, F. Almutairi and H. Rakha, "Eco-Driving at Signalized Intersections: A Multiple Signal Optimization Approach," in IEEE Transactions on Intelligent Transportation Systems, vol. 22, no. 5, pp. 2943-2955, May 2021, doi: 10.1109/TITS.2020.2978184.
P. Zhou, Z. Fang, H. Dong, J. Liu and S. Pan, "Data analysis with multi-objective optimization algorithm: A study in smart traffic signal system," 2022 IEEE 15th International Conference on Software Engineering Research, Management and Applications (SERA), London, UK, 2022, pp. 307-310, doi: 10.1109/SERA.2017.7965743.
H. Wang, M. Zhu, W. Hong, C. Wang, G. Tao and Y. Wang, "Optimizing Signal Timing Control for Large Urban Traffic Networks Using an Adaptive Linear Quadratic Regulator Control Strategy," in IEEE Transactions on Intelligent Transportation Systems, vol. 23, no. 1, pp. 333-343, Jan. 2022, doi: 10.1109/TITS.2020.3010725.
Su, Wei, Chaoxu Mu, Lei Xue, Xiaobao Yang, and Song Zhu. "An improved traffic coordination control integrating traffic flow prediction and optimization." Engineering Applications of Artificial Intelligence 143 (2025): 109969.
Nayeri, Omid, Abbas Babazadeh, Elham Golpayegani, and Mohammad Nayeri. "Traffic signal optimization using hierarchical reinforcement learning: incorporating pedestrian dynamics and flashing light mode." Transportation Planning and Technology (2025): 1-30.
Wang, Lijuan, Guoshan Zhang, Qiaoli Yang, and Tianyang Han. "An adaptive traffic signal control scheme with Proximal Policy Optimization based on deep reinforcement learning for a single intersection." Engineering Applications of Artificial Intelligence 149 (2025): 110440.H. Wang, H. Chen, Q. Wu, C. Ma and Y. Li, "Multi-Intersection Traffic Optimisation: A Benchmark Dataset and a Strong Baseline," in IEEE Open Journal of Intelligent Transportation Systems, vol. 3, pp. 126-136, 2022, doi: 10.1109/OJITS.2021.3126126.
Azad‐Manjiri, Meisam, Mohsen Afsharchi, and Monireh Abdoos. "DDPGAT: Integrating MADDPG and GAT for optimized urban traffic light control." IET Intelligent Transport Systems 19.1 (2025): e70000.
Zhang, Gongquan, Fengze Li, Dian Ren, Helai Huang, Zilong Zhou, and Fangrong Chang. "Cooperative control of self-learning traffic signal and connected automated vehicles for safety and efficiency optimization at intersections." Accident Analysis & Prevention 211 (2025): 107890.

## Slide 16
Thank You